## Slide 1: .LIB
By
Md Fayaaz Shareef
Batch 39

## Slide 2: What is lib?
.lib file is a Library file. Which is one of the input file for Physical Design (PD).
.lib file are provided by vendors.
.lib is basically a timing model which contains cell delays, transition, setup time and hold time requirements.
CCS and NLDM techniques are used to generate .lib files.

## Slide 3: What is CCS and NLDM?
CCS
CCS means Composite Current Source.
It is a current source used for driver modeling.
It has 20 variables to account input slew and output load data.
More accurate.
CCS is larger.
Run time is more
NLDM
NLDM means Non Linear Delay Model.
It is a voltage source used for driver modeling.
It has only 2 variables which are not sufficient for modeling the nonlinearity of any circuit.
Less accurate.
NLDM is smaller.
Run time is less.

## Slide 4: What lib file contain?
Functionality information
- It contain functionality information of cells. Cells like standard cells and macros.
Timing information
- It contain timing information of setup and hold time requirements.
Power information
- It contain power information like power switching, leakage power and internal power

## Slide 5
PVT Corners
- PVT means Process Voltage Temperature
- To process the chips after fabrication we check all possible scenarios to make the chip
work.
- The design needs to be tested for certain PVT corners but for every PVT corner, the
timing of cells are different.

## Slide 6
Cell delay information
- It contain input transition and output load based on lookup table.
Output Load
Input transition

## Slide 7: Unit attributes in .lib file
Time unit
Current unit
Voltage unit
Leakage power unit
Capacitive load unit
Slew rate : Lower and upper limit values are defined in terms of percentage for both rise and fall time
Input and Output threshold for rise and fall time.

## Slide 8
Look Up table
It is defined for different parameters like delay, hold, passive energy, recovery, removal, setup with different matrix.
Wire Load
Resistance
Capacitance
Area
Slope
Fanout length

## Slide 9
Cell
Cell Name
Cell footprint
Power characteristics like Leakage power and Cell leakage power.
Area
Driven waveform of rise time and fall time.
Pg pins of VSS & VDD.
Pin connections

## Slide 10
Pins
Fanout load
Related power pin and groun pin
Directions
Fall and rise capacitance
Fall and rise capacitance range
Internal power
Rise and fall power
Timing
Related pins
Timing type
Timing sense
Cell rise and cell fall
Fall transition and rise transition

## Slide 11
Example:
Cell (AND2_3){
area: 8.000
pin (o){
direction: output;
timing 0{
related _pin: "A";
rise _propagation ( )
}
rise_transition ( )
}
function: "(A & B)";
max_cap;
min_cap;
}
pin (a) {
related power pin = "VDD";
related ground pim = "VSS";
direction : input;
max capacitance : 8 ;
}

## Slide 12: THANK YOU