## Slide 1
DEF- DESIGN EXCHANGE FORMAT

## Slide 2
DEF’s full form is Design Exchange Format (DEF). It is used to represent the Physical layout of an Integrated Circuit (IC) in ASCII format.
It represents the netlist and circuit layout. We used DEF along with LEF (Library Exchange Format) to represent complete physical layout of an integrated circuit while it is being designed.
DEF was developed by Cadence Design Systems
Basically, the DEF file contains information about where macros, standard cells, I/O pins, and other physical things should be placed. It includes all coordinate information for any designed physical shape.

## Slide 3
DEF is a source of input for a number of phases. In order to offer details on the macro location, IO ports, and block shape, Floorplan DEF is provided during the import design step.
DEF file has two main things logical and physical design data Logical design data include internal connectivity which is represented by netlist, grouping information, and physical constraints, while Physical design data information includes placement location and orientation of geometry.
It represents a netlist, component placements and routing information. However, it does not contain any information on the used components. For this type of information DEF is normally used in conjunction with LEF.
The connection of a large number of components is the main focus of the design of the DEF file format.

## Slide 4
Using DEF in the Layout Editor The DEF file format is strongly connected with the LEF file format. Both files are needed for the correct display of a physical design.
SCANDEF file contains the scan chain information of the design and this file need to be read during PnR.
.def and .fp are common factors
Def contains placements info of standard cells, macros , routes input ,output ports
(or) pin locations ,blockages etc.
It generally defines die size , connectivity, pin placement , power domain information

## Slide 5
FLOORPLAN STAGE
OPEN_LIB LAB2_floorplan …../orCA _ TOP
OPEN_BLOCK oRCA _ top
Write_def filename.def
Sh gvim filename.def
PLACEMENT STAGE
OPEN_LIB LAB3_placement …../orCA_TOP
OPEN_BLOCK Orca_top
Write_def filename.def
Sh gvim filename.def
Version
Dividechar
Busbitchars
Design
Units
Diearea
Components
Pins
nets
Enddesign
endnets
Version
Dividechar
Busbitchars
Design
Units
Diearea
Row
Tracks
Vias
Specialnets
Scanchains
Components
pins

## Slide 6
Cts stage
OPEN_LIB LAB3_placement …../orCA_TOP
OPEN_BLOCK Orca_top
Write_def filename.def
Sh gvim filename.def
Routing stage
OPEN_LIB LAB3_placement …../orCA_TOP
OPEN_BLOCK Orca_top
Write_def filename.def
Sh gvim filename.def
Version
Dividechar
Busbitchars
Design
Units
Diearea
Row
Tracks
Vias
Specialnets
Scanchains
Components
Pins
nondefaultrules
Version
Dividechar
Busbitchars
Design
Technology
Units
Row
Tracks
Cell grid
Vias
Nondefaultrules
Components
Pins input ouput
Blockage
Fills
Nets
Groups
Scanchains
macros
End design

## Slide 7
Technology file(.tf)

## Slide 8
File Format :- .tech lef (Cadence) or .tf(In Synopsys)
Provided by :- Fab House
Description :- It describes the units, drawing patterns, layers,design rules, vias, and parasitics resistance and capacitance of the manufacturing process .
Technology file contains all the details of metal layers information , vias as their design rules.
Technology file is most critical input for physical design tools
A technology file, denotes as .tf ,is a file used to describe the fabrication process and design rules used in semiconductor manufacturing .
It typically contains information about layer materials design constraints and other high level parameters related to manufacturing process.

## Slide 9
It contains information
Techonology
Name
Date dielectric
Unit time name
Time precision
Using length name
Length precision
Grid resolution
Unit voltage name
Voltage precision
Unit current name
Current precision
Unit power name
Power precision
Unit resistance name
Resistance precision
Min edge mode
Colour
Name
Rgb defined
Red intensity
Blue intensity
Green intensity
Stipple
Width
Height
pattern
Layer
Layer number
Mask name
Is default layer
Visible
Selectable
Blink
Colour
Line style
Pattern
Pitch
Default width
Min width
Min spacing
Contactcode
Contact code number
Cut layer
Lower layer
Upper layer
Is default contact
Cut width
Cut height
Upper layer width
Lower layer height
Min cut spacing
Max num rows non turning
Unit min resistance
Unit max resistance